OLIMEXINO-2560
Users manual

Rev.1	June 2019
olimex.com
# OLIMEXINO-2560 features
OLIMEXINO-2560 is Arduino Mega 2560 like board with ATMega2560 processor and these features:
- ATMega2560 AVR processor
- 256 KB Flash, 8KB SRAM, 4KB EEPROM
- 88 GPIO
- micro USB connector
- USB-Serial converter with CH340T for Arduino IDE programming via USB
- 4 status LEDs – Power (green), Status (yellow), Tx (green), Rx (red)
- micro SD card for file storage
- Works on 5V and 3.3V (jumper selectable)
- Programmable with Arduino IDE (www.arduino.cc)
- Power supply is 6-15VDC for 5V operation
- Power supply is 5-15VDC for 3.3V operation
- Can be powered by USB connector power
- UEXT connector with power supply enable/disable
- Reset Button
# OLIMEXINO-2560 component locations
## GPIO Digital1

## GPIO Digital2

## GPIO Serial

## GPIO I2C

## GPIO Digital3

## GPIO Digital4

## GPIO Digital5

## GPIO Digital6

## GPIO Digital7

## GPIO Digital8

## GPIO Analog 1

## GPIO Analog 2

## UEXT

## UART (CH340T USB-to-Serial signals)

## ISP AVR programming connector

# LEDs

# Jumpers
## J1
J1 selects at what voltage OLIMEXINO-2560 works 5V (1-2 pin) or 3.3V (2-3pin).
Note that if you attach UEXT board the power supply must be 3.3V or the UEXT board will be damaged.

## J2
J2 jumper selects if Arduino can Reset and program board automatically if pin 1-2 are shorted

# Using Digital GPIOs
You can set any of the Digital GPIOs as input or output using their names:

pinMode(D33,INPUT);	//D0-D53, PH2..PE2
value = digitalRead(D33);
pinMode(D13,OUTPUT);
digitalWrite(D13,HIGH);

# Using Analog GPIOs
value = analogRead(A7); //A0..A15
analogWrite(D44,128);	//PWM GPIOs D2..D13, D44..D46, value 0..255
# Power supply requirements
OLIMEXINO-2560 can be powered by USB port or External Power supply, Jack inner pin 2 mm and external diameter 5.5mm. Switching between power supplies is automatically, i.e. if external power supply is applied USB power supply is not used.
# Revision History
1.00 June 2019